## Slide 1: ASSEMBLY LANGUAGE
DATA TRANSFER INSTRUCTIONS
-MOV, XCHG Instructions

## Slide 2: MOV Instruction
#
In JAVA, assignments are
x = 42;
y = 24;
z = x + y;
How do we represent in assembly language?

## Slide 3: MOV AX, 42
#
MOV BX, 24
Syntax:
MOV destination, source
Data is copied from the source to the destination, so the source operand is not changed
MOV Instruction

## Slide 4: MOV Instruction
#
Possible combinations of operands: mov reg, reg
mov reg, immediate mov reg, memory
mov memory, immediate
mov memory, reg

## Slide 5: MOV Instruction
#
The MOV instruction allows us to copy contents of one register into another register.
Register operands
  A move involving only registers is the fastest type.
  Registers should be used when an instruction must execute quickly.
    MOV AX,BX
    MOV DL, AL
    MOV BX,CX

## Slide 6: MOV Instruction
Example:
#
MOV BX, 2 MOV CX, BX
More examples:
MOV BX, 4 ;copy number 4 into register BX MOV AX, BX ; copy contents of BX into AX MOV CX, AX ; copy contents of AX into CX

## Slide 7: Limitations of MOV
#
An immediate value cannot be moved into a segment register directly (ie: MOV DS, 10)
Segment registers cannot be copied directly (ie: MOV ES, DS)
A memory location cannot be copied into another memory location
(ie: mov aNumber, aDigit).
CS and IP may never be destination operands
The source and destination operands must be the same size.
If the source is immediate data, it must not exceed 255(FFh) for an 8-bit destination or 65,535 (FFFFh) for a 16-bit destination.

## Slide 8: XCHG Instruction
#
Swaps two values . The general form is XCHG operand1, operand2
Can be in the following form:
XCHG reg, mem XCHG reg, reg
The order of the operand is not important ie: XCHG AX, BX == XCHG BX, AX
XCHG instruction does not modify any flags

## Slide 9: XCHG Instruction
#
This instruction provides a speed advantage (especially in sorting applications).
Example:
MOV AX, 24h ; copy 24h into AX MOV BX, 23h ; copy 23h into BX
XCHG AX, BX ; swaps the value of AX and BX